## Slide 1: Networking
ECT 424/IS 324
Module 2

## Slide 2: IT Components
Underlying Infrastructure (cabling)
Local Area Networks (connected devices)
Wide Area Networks (collections of networks)
Data Centers (devices providing services)
Internet access (Cloud and remote access)

## Slide 3: Last Class
We covered
  Shifting Roles of IT
  Models
    OSI vs TCP/IP
  Nodes (hardware)
    Computer Parts
Make sure you are making your D2L comments (2/week)

## Slide 4: Recap - Shifting Skills in IT
With a Push from Cloud Computing, IT is becoming more of a SUPPLY CHAIN than traditional infrastructure.
That is why three-quarters (72%) of IT managers say their IT organizations are focusing more time on managing outsourced IT or cloud services providers than they were five years ago.
Notes: More than half (54%) of the respondents in the Global Market Pulse Survey acknowledged that the current
value of IT is largely defined by its role as the owner and operator of the IT infrastructure.
Within two years, however, respondents believe the primary value of IT will come from managing the IT supply chain.
This explains why nearly three-quarters (72%) of IT managers say their IT organizations are focusing more time
on managing outsourced IT or cloud services providers than they were five years ago.

## Slide 5: Recap - Shifting Skills in IT
“The IT center of the future is one that combines cloud when necessary, on premise when it’s useful, virtualization when applicable.
All these resources need to connect together to best serve business needs.”
— Gerardo Dada, Director of Product Marketing Rackspace Hosting
The IT supply chain manager will manage the service delivery of IT from both internal and external sources
The importance of business knowledge, process standardization, expertise, cloud expertise, the ability to manage service providers, and communication skills has increased for the majority of IT respondents (particularly in the U.S.)

## Slide 6
OSI Model |  |  | 
 | Data unit | Layer | Function
Host layers | Data | 7. Application | Network process to application (end user layer)
 |  | 6. Presentation | Data representation, syntax layer, encryption and decryption, convert machine dependent data to machine independent data
 |  | 5. Session | Interhost communication (logical ports)
 | Segments | 4. Transport | End-to-end connections and reliability, (Host to Host, Flow control)
Media layers | Packet | 3. Network | Path determination and logical addressing (“letter” containing IP address)
 | Frame | 2. Data Link | Physical addressing (“Envelopes” contain MAC address)
 | Bit | 1. Physical | Media, signal and binary transmission (cables, hubs etc)
Notes: Transport Set
Layer 1: Physical - This is the level of the actual hardware. It defines the physical characteristics of the network such as connections
Layer 2: Data Link- In this layer, the appropriate physical protocol is assigned to the data. Also, the type of network and the packet sequencing is defined.
Layer 3: Network - The way that the data will be sent to the recipient device is determined in this layer. Logical protocols, routing and addressing are handled here.
Layer 4: Transport - This layer maintains flow control of data and provides for error checking and recovery of data between the devices.
Application Set
Layer 5: Session - Layer 5 establishes, maintains and ends communication with the receiving device.
Layer 6: Presentation - Layer 6 takes the data provided by the Application layer and converts it into a standard format that the other layers can understand.
Layer 7: Application - This is the layer that actually interacts with the operating system or application whenever the user chooses to transfer files, read messages or perform other network-related activities.
Bit is the basic unit of information
Frame is a digital data transmission unit
Network Packet is a formatted unit of data
Network segment is a portion of a computer network

## Slide 7: Loosely translated Tweet using the OSI model

## Slide 8
OSI Model |  |  | 
 | Data unit | Layer | Function
Host layers | Data | 7. Application | Network process to application (end user layer)
 |  | 6. Presentation | Data representation, syntax layer, encryption and decryption, convert machine dependent data to machine independent data
 |  | 5. Session | Interhost communication (logical ports)
 | Segments | 4. Transport | End-to-end connections and reliability, (Host to Host, Flow control)
Media layers | Packet | 3. Network | Path determination and logical addressing (“letter” containing IP address)
 | Frame | 2. Data Link | Physical addressing (“Envelopes” contain MAC address)
 | Bit | 1. Physical | Media, signal and binary transmission (cables, hubs etc)
Physical
NW Access
Internet
Host to Host
Process
DoD Model

## Slide 9: This Class
IT Components
  LANS
    Parts
  Why and how they are used in the enterprise
  WANs
    Types
    Services

## Slide 10: Definitions
Communications
  Packet Switched
    Packet switching entails packaging data in specially formatted units (packets ) that are routed from source to destination using network switches and routers . Each packet contains address information that identifies the sending computer and intended recipient.
  Circuit Switched
    Circuit-switching is where a physical path is obtained for and dedicated to a single connection between two end-points in the network for the duration of the connection.
Media
  Types
  Structured Cabling Design
LAN, WLAN
WAN
Notes: Packet switching entails packaging data in specially formatted units (packets ) that are routed from source to destination using network switches and routers . Each packet contains address information that identifies the sending computer and intended recipient.
Circuit-switching is where a physical path is obtained for and dedicated to a single connection between two end-points in the network for the duration of the connection.

## Slide 11: Comparison of Packet and circuit Switching
Notes: Nowadays there is a convergence of these two types (think VoIP) of communication switching but primarily packet switching has traditionally been for data and circuit switching has been for voice

## Slide 12: Let’s start with the Local Network
What makes a local area network, local?
And what do tennis shoes have to do with it?

## Slide 13: LANs – a brief history
Sneakernet
Small LANs
Enterprise LANs

## Slide 14: Parts
What are the parts of a local area network?
  Physical connections (media)
  Nodes
  Interconnectivity Hardware (hubs, switches, routers)
  Customer Premise Equipment

## Slide 15: What Services are provided by the LAN
Access
Sharing (of resources)
  Data
  Applications,
  Storage
  Centralized access control/authentication
  Printing
  Internet
Applications

## Slide 16: Enterprise Applications
Depending on the enterprise
  Transaction Processing systems
  ERP
  Information Systems
  Email
  Streaming video/audio (training, meetings)
  Collaboration tools

## Slide 17: Cabling

## Slide 18: Reality Check
While we are starting at the bottom of the OSI model
In reality you would start at the TOP
  Define the types of applications that must be used in the organization
  Define the quantity and quality of the traffic generated by those applications
  These will inform all of the decisions – Top Down

## Slide 19
Layer Decision: Cabling – Wired or wireless (i.e. – guided and unguided)?
If wired, what kind of cabling do we use?
  Twisted pair Cu
  Coaxial (coax) -- not really a choice for LAN
  Fiber Optic (fiber)
Physical Layer

## Slide 20
Media
Guided
Media
Unguided
Media
Coax
Cable
Twisted
Pair
Fiber
Optics
Infrared
Radio
Frequency

## Slide 21
http://www.infocellar.com/networks/cables/twisted-pair-cables.htm
Two wiring plans (stds) 568A & 568B

## Slide 22: Cable Types
Notes: Straight through cabling is most common.
Cross over cabling is used when connecting two hosts– For Example two computers
Roll over cabling (Cisco console) is used to connect to a devices console port to make programming changes to the device. They are not used to carry data.

## Slide 23: Cu (copper) Cabling Type Standards
Cat 1: Retired. Previously used for POTS telephone communications, ISDN and doorbell wiring. Max rate 1 Mbps
Cat 2: Retired. Was used on IBM token ring networks. Max rate 4 Mbps
Cat 3: Historically popular for 10 Mbit/s Ethernet networks. Max rate 16 Mbps
Cat 4: Retired. Was frequently used on IBM token ring networks. Max rate 20 Mbps
Cat 5: Is used on 100 BaseT Ethernet networks, with four pair wires may be used for GigaE, runs at 100 Mhz but…
Cat 5e: Provides more shielding and is the better choice for GigaE networks. Max rate is 1000 Mbps (still running a 100 Mhz).
Cat 6: May provide better than GigaE performance (up to 250 MHz).
Cat 6a: Specification for 10 Gbps applications (up to 500 MHz).
Cat 7: Future specification for transmission at frequencies up to 600 MHz.
Cat 7a: Future specification to 1,000 MHz
CU=Copper

## Slide 24: Transmission media: coaxial cable
One copper conductor within a tubular conducting shield. The generated energy fields are contained by the outer conductor.
A
B
C
D

## Slide 25: Transmission media: fiber optic cable
One or more optical “light pipes” within a tubular conductor. Cladding contains laser-generated light within the optic channel. Lasers are modulated with digital signals.

## Slide 26: Modes of Fiber
Single Mode
Multi-Mode
http://www.youtube.com/watch?v=VpBX_GpuQUA&feature=relmfu
http://www.youtube.com/watch?v=mUBRjiVhJTs
Bendable fiber
Notes: STEP-INDEX MULTIMODE FIBER has a large core, up to 100 microns in diameter. As a result, some of the light rays that make up the digital pulse may travel a direct route, whereas others zigzag as they bounce off the cladding. These alternative pathways cause the different groupings of light rays, referred to as modes, to arrive separately at a receiving point. The pulse, an aggregate of different modes, begins to spread out, losing its well-defined shape. The need to leave spacing between pulses to prevent overlapping limits bandwidth that is, the amount of information that can be sent. Consequently, this type of fiber is best suited for transmission over short distances, in an endoscope, for instance.
GRADED-INDEX MULTIMODE FIBER contains a core in which the refractive index diminishes gradually from the center axis out toward the cladding. The higher refractive index at the center makes the light rays moving down the axis advance more slowly than those near the cladding. Also, rather than zigzagging off the cladding, light in the core curves helically because of the graded index, reducing its travel distance. The shortened path and the higher speed allow light at the periphery to arrive at a receiver at about the same time as the slow but straight rays in the core axis. The result: a digital pulse suffers less dispersion.

## Slide 27: Centralized Fiber LAN

## Slide 28: Fiber Optic vs. Copper (TP)
Advantages
SPEED: Fiber optic networks operate at high speeds - up into the gigabits
BANDWIDTH: large carrying capacity
DISTANCE: Signals can be transmitted further without needing to be "refreshed" or strengthened.
RESISTANCE: Greater resistance to electromagnetic noise such as radios, motors or other nearby cables. Very low error rates.
SECURITY: Not electromagnetic; harder to “listen in” on data transfer. Splices can be easily detected.
MAINTENANCE: Fiber optic cables costs much less to maintain.
Disadvantages
COST: Components are expensive. Installation is expensive. Special test equipment is required.
FRAGILE: Susceptible to damage during installation (or disruption.)
STANDARDIZATION: Less standardization across vendors than with copper.
FLEXIBILITY: Cable can’t bend around tight corners.

## Slide 29: Good Places for Fiber
Industrial Networks
  With lots of Electromagnetic Interference (EMI)
  Less than copper in conduit
Long cable runs
  Anything > 90 m (~270ft) and you’re almost always better off with fiber

## Slide 30: Drawbacks?
Fiber electronics (read switchports) will always be more expensive
  If you change out the switch several times over the life of the cable plant – the cost could be significant
PoF – is still not as efficient as over copper
  (pof = power over fiber)
Notes: Fiber is a bad conductor of electricity so it is NOT ideal wherever power is ALSO required.

## Slide 31: Is Copper Always less Expensive?
Well, it depends
  As compared to what?
    Per bit , per device, per foot?
  What is included in the cost?
    Just cable, ports on devices, repeaters, maintenance, TCO?

## Slide 32: Structured Cabling Design
TIA/EIA 568A – Structured Cabling Standard
  TIA is the Telecommunications Industry Association which is an offshoot of the Electronic Industries Alliance
It is: Sets of rules that guide for:
  size of room
  height of ceiling
  lighting at 1 m from floor
  materials used in the telcom room through the floors, walls, and ceiling

## Slide 33: How NOT to install cable

## Slide 34: Cable Design and Management
What’s a Cable plant?
  Hardware comprising enterprise-wide cabling system
What’s Structured cabling?
  Method for uniform, enterprise-wide, multivendor cabling systems

## Slide 35
Figure 3-39 TIA/EIA structured cabling in an enterprise
In telephony, the demarcation point is the point at which the public switched telephone network ends and connects with the customer's on-premises wiring.
Notes: In telephony, the demarcation point is the point at which the public switched telephone network ends and connects with the customer's on-premises wiring.

## Slide 36: Demarcation
©Cisco 2010
Internationally the Network Termination Unit (NTU) is owned by the service provider.
In the US the service provider doesn’t supply the network termination unit rather the Channel/Data Service Unit (CSU/DSU) is owned by the company/organization.
Notes: DCE is the Distributed Computing Environment

## Slide 37: Cabling Design
Access
Distribution
Core/Backbone
Routing, policy based distribution, filtering happen here
Really fast switching of packets to final destination – no routing here, no filtering
©Cisco 2010
Notes: Also known as the backbone of the network; this is the heart of the network and is responsible for switching huge amounts of traffic very reliably. It must offer high reliability, provide redundancy, provide fault tolerance and avoid slowing traffic down by filtering it in any way.
The distribution layer allows communication between the core and access layers. Packets are manipulated at this layer. The distribution layer should perform certain services such as security, workgroup access routing between LANs, traffic filtering, and redistribution.
The access layer/the desktop layer, this is the point at which end users connect to the network. The access layer allows user access to local segments on the network. Functions performed here include segmenting the network into smaller chunks, sharing bandwidth and local policies for network traffic control.
Breaking networks down into specific layers helps us to understand how they work and also which devices should be performing which functions and features.

## Slide 38: Wider view Hierarchical Design (functional areas)
©Cisco Enterprise Architecture Modules
Enterprise Architecture
Notes: Enterprise Campus Functional Area
The enterprise campus functional area is intended to be the center of the network design, located at a single location where several different core elements are located and are accessed from all other parts of the network.
Enterprise Edge Functional Area
The enterprise edge functional area is responsible for the aggregation of several different off-campus elements as well as the routing of this traffic into the campus core module within the Enterprise Campus Functional area.
Service Provider Functional Area
The service provider functional area is responsible for connectivity into Service Provider networks. This includes a number of different connectivity options, from Internet access through Public Switched Telephone Network (PSTN) access.
Remote Functional Area
The remote functional area is responsible for connectivity of a number of different remote functional elements, including enterprise branches (connecting through a service provider), enterprise data centers, and enterprise teleworkers.

## Slide 39: L1 & L2 Networking Connectivity Devices
Hubs (Layer 1)
Bridges (L2, up to 16 ports)
Switches (glorified bridges with up to 100 ports)
Notes: Hub is the least expensive, least intelligent, and least complicated. Its job is very simple – anything that comes in one port is sent out to the others.

## Slide 40: Shared Media environment
data
Layer-1 device
Repeater: 2-port hub
  Connectivity device that regenerates digital signal
    Compensates for Noise (Attenuation)
Hub: multi-port repeater, half-duplex
Signal received on one port is broadcast to all other ports
This is mostly what TRU has now, running on 10 Mbps cable.

## Slide 41: Hubs (multi port repeaters)
A Hub is the least expensive, least intelligent, and least complicated. Its job is very simple – anything that comes in one port is sent out to the others.
If a message comes in for computer “A”, And when computer “A” responds, its response also
that message is sent out all the other ports, goes out to every other port on the hub
regardless of which one computer “A” is on

## Slide 42
Internetworking Devices
Repeater
Eg. A Hub
Note: A repeater connects segments of a LAN together.
It forwards every packet; it has no filtering capability.
0011001010
0011001010

## Slide 43: Bridges
Like a repeater, a bridge has typically a single input and single (sometimes multiple) output port
But… Unlike a repeater, it can interpret the data it retransmits
Layer-2 device (reads L 2 addresses)
Advantages over repeaters and hubs
  Improved network performance
  Breaks up collision domains (the portion of the network in which collisions of frames can occur)
  Each interface becomes a collision domain
Notes:     A collision domain is, as the name implies, a part of a network where packet collisions can occur. A collision occurs when two devices send a packet at the same time on the shared network segment. The packets collide and both devices must send the packets again, which reduces network efficiency.

## Slide 44
Bridge:
Connect LAN segments together
Read only the destination address of each Ethernet packet or Token Ring frame for maximum speed and efficiency
has a table used in filtering decisions
H
H
0011001010
0011001010
Forward/Learn Process
Notes: Connect two parts of the same network. Read only the destination address of each Ethernet packet or Token Ring frame for maximum speed and efficiency.

## Slide 45: Switches
These devices are Bridges with “marketing”
They operate in much the same way (but in hardware, and MUCH faster)
Most are full duplex
They are optimized to filter and forward VERY quickly
  Cut-thru
  Store and forward
  Fragment free

## Slide 46: Switches
A Switch does essentially what a hub does, but more efficiently.
Initially, a switch knows nothing and simply sends on incoming messages to all ports
Even accepting that first message, however, the switch has learned something – it knows on which connection the sender of the message is located. Thus, when machine “A” responds to the message, the switches only need to send that message out to the one connection

## Slide 47: Switches
In addition to sending the response through to the originator, the switch has now learned something else – it now knows on which connection machine “A” is located. That means that subsequent messages destined for machine “A” need only be sent to that one port

## Slide 48: Network Topology Forms
What are the pathways packets take?

## Slide 49: Simple Physical Topologies
A terminated bus topology network
Physical topology
  Physical layout of a network
A Bus topology consists of a single cable, called a bus, connecting all nodes on a network without intervening connectivity devices

## Slide 50: Star Topology
Every node on the network is connected through a central device
  Physical medium
    Twisted pair or fiber-optic cabling
Most popular fundamental layout

## Slide 51: Star-wired Bus Topology
In a star-wired bus topology, groups of workstations are star-connected to hubs and then networked via a single bus
Bus (no nodes)

## Slide 52: Network topology: Mesh
Advantages/Disadvantages
Decentralized
Expensive
Reliable and resilient
Network can span large distances
Increase capacity by adding more nodes
Fixed or mobile devices

## Slide 53: Backbone Networks
The backbone network is an important architectural element for building enterprise networks.
It provides a path for the exchange of information between different LANs or subnetworks.
A backbone can tie together diverse networks in the same building and/or different buildings and campus environments, or over wide areas.
It is mostly cabling connecting hubs, switches, routers
There is significantly more throughput - “bigger pipes”
Large organizations usually have
  Fiber-optic backbone
  Cat 5e or better for hubs, switches
Enterprise-wide network backbones
  Complex, difficult to plan
  Affect the Entire organization
  Are a significant building block

## Slide 54: Collapsed Core Backbone Network
©Cisco 2010
Enterprise Edge
Collapsed ::= divide a single collision domain into multiple ones
Uses a router or switch as the single central connection point for multiple sub networks
ease of management since the backbone is in a single location and in a single box
since the backbone essentially uses internal switching matrix of the box, proprietary, high performance technology can be used.
Notes: Single central connection point for multiple subnetworks. Uses a router or switch
Router with multiprocessors
Risks are
Central router failure
Routers may slow data transmission
Advantages
  Interconnect different sub network types
  Central management

## Slide 55: Intranet Server Farm
©Cisco 2010

## Slide 56: Enterprise Architecture
©Cisco 2010

## Slide 57
Do we have a universal standard for communication at the lower layers of the model inside the enterprise?
Network Access Layer
Ethernet DSL ISDN FDDI PPP
Ethernet is pretty much the only standard in use today

## Slide 58: Wireless Local Area Networking
(Wi-Fi)

## Slide 59: The Wireless Spectrum
This Auction by the FCC happened in 2008. the next Auction for the 600Mhz spectrum will occur in 2015
Guess who were the major participants in the auction?
Why?
Who ended up buying most of the 700Mhz spectrum?
Notes: Continuum of electromagnetic waves
  Data, voice communication
  Arranged by frequencies
    Lowest to highest
  Spans 9 KHz and 300 GHz
Wireless services associated with one area
FCC oversees United States frequencies
ITU oversees international frequencies
  Air signals propagate across borders

## Slide 60: Characteristics of Wireless Transmission
Notes: Similarities with wired
  Layer 3 and higher protocols
  Signal origination
    From electrical current, travel along conductor
Differences from wired
  Signal transmission
    No fixed path, guidance
Antenna
  Signal transmission and reception
  Same frequency required on each antenna
    Share same channel

## Slide 61: WiFi Signal Propagation
LOS (line-of-sight)
  Signal travels
    In straight line, directly from transmitter to receiver
Obstacles affect signal travel
  Pass through them
  Absorb into them
  Subject signal to three fading phenomena
    Reflection: bounce back to source
    Diffraction: splits into secondary waves
    Scattering: diffusion in multiple different directions
Notes: Multipath signals
  Wireless signals follow different paths to destination
  Caused by reflection, diffraction, scattering
  Advantage
    Better chance of reaching destination
  Disadvantage
    Signal delay

## Slide 62: Signal Degradation
Fading
  Change in signal strength
    Electromagnetic energy scattered, reflected, diffracted
Attenuation
  Signal weakens
    Moving away from transmission antenna
  Correcting signal attenuation
    Amplify (analog), repeat (digital)
Noise
  Significant problem
    No wireless conduit or shielding possible
Notes: Fading signal problem

## Slide 63: Frequency Ranges
2.4-GHz band (older)
  Frequency range: 2.4–2.4835 GHz
  11 unlicensed communications channels
  Susceptible to interference
Unlicensed
  No FCC registration required
5-GHz band (newer)
  Frequency bands
    5.1 GHz, 5.3 GHz, 5.4 GHz, 5.8 GHz
  24 unlicensed bands, each 20 MHz wide
  Used by weather, military radar communications

## Slide 64: Narrowband, Broadband, and Spread Spectrum Signals
Defines wireless spectrum use:
  Narrowband
    Transmitter concentrates signal energy at single frequency, very small frequency range (think telephones)
  Broadband
    Relatively wide wireless spectrum band
    bandwidth is shared by more than one simultaneous signal
    Higher throughputs than narrowband
  Spread-spectrum
    Multiple frequencies used to transmit signal
    Offers noise reduction, security and resistance to jamming/interception
  Orthagonol (OFDM)
    Uses multiple carrier frequencies for increased throughput
    OFDM uses many narrow band signals (think digital TV)
Notes:     Orthogonal frequency-division multiplexing (OFDM) is a method of encoding digital data on multiple carrier frequencies. OFDM has developed into a popular scheme for wideband digital communication, whether wireless or over copper wires, used in applications such as digital television and audio broadcasting, DSLbroadband internet access wireless networks, and 4G mobile communications.
The term has been extended to general use, meaning the characteristic of being independent (relative to something else). It also can mean: non-redundant, non-overlapping, or irrelevant. In computer terminology, something - such as a programming language or a data object - is orthogonal if it can be used without consideration as to how its use will affect something else.
FHSS (frequency hopping spread spectrum)
  Signal jumps between several different frequencies within band
  Synchronization pattern known only to channel’s receiver, transmitter
DSSS (direct-sequence spread spectrum)
  Signal’s bits distributed over entire frequency band at once
  Each bit coded
    Receiver reassembles original signal upon receiving bits

## Slide 65: Fixed versus Mobile
Mobile communications wireless systems
  Receiver located anywhere within transmitter’s range
    Receiver can roam
    WiFi and Cellular networks
Fixed communications wireless systems
  Transmitter, receiver locations do not move
  Transmitting antenna focuses energy directly toward receiving antenna
    Point-to-point link results
  Advantage
    No wasted energy issuing signals
    More energy used for signal itself
  Used in Bldg to Bldg communications

## Slide 66: wLAN Architecture
An ad hoc WLAN
An infrastructure WLAN
Notes: Ad hoc WLAN
  Wireless nodes transmit directly to each other
  Use wireless NICs
    No intervening connectivity device
  Poor performance
    Many spread out users, obstacles block signals
Access point (AP)
  Accepts wireless signals from multiple nodes
    Retransmits signals to network
  Base stations, wireless routers, wireless gateways

## Slide 67: wLAN Architecture (cont’d.)
Infrastructure wLAN
  Stations communicate with access point
    Not directly with each other
  Access point requires sufficient power, strategic placement
wLAN may include several access points
  Dependent upon number of stations
  Maximum number varies: 10-100

## Slide 68: 802.11 wLAN Standard
Wireless technology standard
  Describes unique functions
    Physical and Data Link layers
  Differences
    Specified signaling methods, geographic ranges, frequency usages
  Developed by IEEE’s 802.11 committee
Wi-Fi (wireless fidelity) standards
  802.11b, 802.11a, 802.11g, 802.11n, 802.11ac
  Share characteristics
    Half-duplexing, access method, frame format
Notes: Institute of Electrical and Electronics Engineers

## Slide 69: AP Management – Site Survey

## Slide 70: WiFi Access Method
802.11 MAC services
  Append 48-bit (6-byte) physical addresses to frame
    Identifies source, destination
Same physical addressing scheme as 802.3
  Allows easy combination
Wireless devices
  Not designed for simultaneous transmit, receive
  Cannot quickly detect collisions
  Use different access method (CSMA/CA)
Notes: 802.3 is the ethernet standard from IEEE
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)

## Slide 71: Carrier Sense Multiple Access with Collusion Avoidance CSMA/CA
Notes: RTS is request to send
CTS is clear to send

## Slide 72: Collision Avoidance: RTS-CTS exchange
AP
Src
Other Nodes
time
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
defer
DIFS
SIFS
SIFS
SIFS
DIFS= Distributed Coordinated Function IFS
SIFS = Short IFS
Notes: CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Minimizes collision potential
  Uses ACK packets to verify every transmission
    Requires more overhead than 802.3
    Real throughput less than theoretical maximum
RTS/CTS (Request to Send/Clear to Send) protocol
  Optional
  Ensure packets not inhibited by other transmissions
  Efficient for large transmission packets
  Further decreases overall 802.11 efficiency

## Slide 73: Association
Using a SSID (service set identifier)
  Unique character string identifying access point
  In beacon fame information
  Configured in access point
  Better security, easier network management
BSS (basic service set)
  Station groups sharing access point
  BSSID (basic service set identifier)
  Station group identifier
Notes: Packet exchanged between computer, access point
  Gain Internet access
Scanning
  Surveying surroundings for access point
  Active scanning transmits special frame
    Probe
  Passive scanning listens for special signal
    Beacon fame

## Slide 74: Association (cont’d.)
ESS (extended service set)
  Access point group connecting same LAN
    Share ESSID (extended service set identifier)
  Allows roaming
    Station moving from one BSS to another without losing connectivity
When several access points detected
  Select strongest signal, lowest error rate
  Poses security risk
    Powerful, rogue access point
Notes: ESS with several authorized access points
  Must allow station association with any access point
    While maintaining network connectivity
Reassociation
  Mobile user moves from one access point’s range into another’s range
  Occurs by simply moving, high error rate
Stations’ scanning feature
  Used to automatically balance transmission loads
    Between access points

## Slide 75
A network with multiple BSSs forming an ESS

## Slide 76: 802.11g
Affordable as 802.11b
Throughput
  54 Mbps theoretical
  20 to 25 Mbps effective
100 meter node range
2.4-GHz frequency band
  Compatible with 802.11b networks

## Slide 77: 802.11n
2.4-GHz or 5-GHz frequency range
  Same data modulation techniques as b and g
Compared with other 802.11 standards
  Manages frames, channels, encoding differently
    Allows high throughput
802.11n access point with three antennas using MIMO technique
Notes: Ratified October 2009
Manufacturers
  Selling 802.11n-compatible transceivers
Primary goal
  Wireless standard providing much higher effective throughput
Maximum throughput: 600 Mbps
  Threat to Fast Ethernet
Backward compatible with 802.11a, b, g standards
MIMO (multiple input-multiple output)
  Multiple access point antennas may issue signal to one or more receivers
  Increases network’s throughput, access point’s range

## Slide 78: 802.11n (cont’d.)
Maximum throughput dependencies
  Number, type of strategies used
  2.4-GHz or 5-GHz band
  Actual throughput: 65 to 600 Mbps
Backward compatible
  Not all 802.11n features work
Recommendation
  Use 802.11n-compatible devices

## Slide 79: Latest Version 802.11ac
Gigabit throughputs theoretically possible
  290 Mbps and 1300 Mbps
  5 GHz range
Makes use of many n techniques
Evolving standard
Consumer 11/2012
Enterprise 11/2013

## Slide 80: Bluetooth Networks
Ericson’s original goals
  Wireless technology compatible with multiple devices
  Require little power
  Cover short ranges
Aim of Bluetooth Special Interest Group (SIG)
  Refine and standardize technology
  Result: Bluetooth
    Mobile wireless networking standard using FHSS (frequency hopping spread spectrum) RF signaling in 2.4-GHz band

## Slide 81: Bluetooth Networks (cont’d.)
Version 1.1
  Maximum theoretical throughput: 1 Mbps
  Effective throughput: 723 Kbps
  10 meter node difference
  Designed for PANs (personal area networks)
Version 2.0 (2004)
  Different encoding schemes
    2.1-Mbps throughput
  30 meters node difference
  Usage: cellular telephones, phone headsets, computer peripherals, PDAs

## Slide 82: Summary of WLAN Standards
Wireless standards
Notes: 802.11ac is on 5Ghz and has an thoughputs of up to 1300 Mbps (1.3 Gbps)

## Slide 83: Memo 1
What do I want?
  I want you to go out and learn about cabling options for modern local area networks.
  Then demonstrate to me what you learned about LAN cabling by applying that information to the TRU (Times R Us) situation
  I’m interested in knowing what should we do. Remember that is doesn’t have to be all one thing or another. Tell me what you learned.
DePaul Writing Center http://condor.depaul.edu/writing

## Slide 84: Web Assignment 2 --
Secure your hosted site.
Install WordPress into the /SPRING2015 location (it MUST be available at http://yourdomain.suffix/SUMMER2015 or http://yourname.siteground.net/SUMMER2015
Write your first post (your context document)
Submit to D2L dropbox
  Your url in a Word readable document (no PDF for this assignment please). If you must just submit the URL in the comments section of the dropbox and a blank file.

## Slide 85: Website Project -- Discussion
Assignment 1 -- context
  This will define the context for your website
  You may choose to do TRU (the company for the memos) or you may choose to do a personal blog
  In any case you must answer these three questions
    What community do you plan to serve (who will make comments and why)?
    What value would your site provide (why would people return to your site over and over again)?
    Who would be responsible for writing content on your fictional blogsite (besides you, assuming this isn’t about YOU)?

## Slide 86: Discuss

## Slide 87: How do I connect my locations into an Enterprise?
If we run local systems on Local Area Networks
We connect widely separate networks with a
Wide Area Network

## Slide 88: What is a WAN
©Cisco 2010

## Slide 89: WAN Physical Layer Terms
©Cisco 2010

## Slide 90: WAN Options
©Cisco 2010

## Slide 91: WAN Options
©Cisco 2010
Notes: CSU/DSU- Channel Service Unit/Data Service Unit

## Slide 92: WAN Protocols
©Cisco 2010
Notes: HDLC- High Level Data Link Control
PPP –Point to Point Protocol
SLIP-Serial Line Internet Protocol
ATM-Asynchronous Transfer Mode

## Slide 93: Do we have a universal standard for communication at the lower layers of the model outside the enterprise?
Network Access Layer
Ethernet DSL ISDN FDDI PPP
Frame Relay, MPLS (multi protocol label switching), Metro Ethernet, DSL, PPP, ATM
Notes: MPLS – Multi Protocol Label Switching
DSL- Digital Subscriber Line
PPP –Point to Point Protocol
ATM-Asynchronous Transfer Mode

## Slide 94: Leased Lines
Dedicated point to point links
Cost is determined by capacity of the link and the distance from the end points
Inflexible, and expensive
You pay for the link, whether or not data is travelling at link capacity
Highly secure as your data is only stuff on the link

## Slide 95: Types of T-Carriers – Leased Lines
Table 7-1 Carrier specifications
T1 use
  Connects branch offices, connects to carrier
  Connects telephone company COs, ISPs
  Costs vary per region but a rough ballpark about $1000- $1500 per month
T3 use
  Data-intensive businesses
  Costs also vary but can range form $10K-$30K (or even more) per month
  T3 provides 28 times more throughput
  Multiple T1’s may accommodate needs

## Slide 96: T- Carrier
How much throughput do I need?
  T1: good for about 25 users doing regular office work (~5 power users)
  Bundle T1s to increase capacity
  T3 (28 T1s): ~600 regular users, ~150 power users

## Slide 97: How does data get from one point to another?
Circuit Switching is when two nodes establish a dedicated communication channel for the duration of a session.
The Public Switched Telephone Network (PSTN) uses this (well, used to).
Packet Switching is when information is sent across shared channels inside of blocks (or packets).
The Internet uses this.

## Slide 98: Circuit vs Packet
©Cisco 2010
Circuit is DEDICATED and SESSION BASED
Circuit goes via dedicated path
packet IS BLOCKS OF DATA (think internet)
Packet finds the shortest distance through the network

## Slide 99: Circuit Switching
Connection established between two network nodes
  Before transmitting data
Dedicated bandwidth
All Data follows same path selected initially by switch
Monopolizes bandwidth while connected
  Resources wasted
Uses
  Live audio, videoconferencing
  Home modem connecting to ISP

## Slide 100: Packet Switching
Most popular
Breaks data into packets before transporting
Packets
  Travel any network path to destination
  Find fastest circuit available at any instant
  Need not follow each other
  Need not arrive in sequence
  Must be Reassembled at destination
    Requires speedy connections for live audio, video transmission

## Slide 101: Packet Switching
Advantages
  No wasted bandwidth
  Devices do not process information
Examples
  Ethernet networks
  Internet

## Slide 102: Frame Relay Overview
  Virtual circuit connections
  One physical circuit
  Multiple virtual circuits
Connection-oriented service
  Permanent Virtual Circuit (PVC)
Frame Relay
Router
CSU/DSU
DCE or Frame Relay Switch
Ethernet LAN
Provider network
Notes: Frame relay is a standardized wide area network technology that specifies the physical and logical link layers of digital telecommunications channels using packet switching methodologies
Frame relay puts data in a variable-size unit called a frame and leaves any necessary error correction (retransmission of data) up to the end-points, which speeds up overall data transmission. For most services, the network provides a permanent virtual circuit (PVC), which means that the customer sees a continous, dedicated connection without having to pay for a full-time leased line, while the service provider figures out the route each frame travels to its destination and can charge based on usage.

## Slide 103: Frame Relay (cont.)
Address: Data Link Connection Identifier (DLCI), 10-bit, local significance.
CIR (committed information rate)
  Guaranteed minimum amount of bandwidth selected when leasing a frame relay circuit
  Can burst higher than CIR
  Users get more than they pay for.
CIR
(768k)
burst
(512k)

## Slide 104: MPLS
Multi-Protocol Label Switching
  A more efficient way to forward and route packets
Label Edge Router (LER)
  Analyzes each packet on arrival to the MLPS network and puts on a wrapper which tells each router where to forward the packet without reading the header (just the wrapper)
Label | Traffic class/QOS/ECN | TTL | BOS
20 bits | 3 bits | 8 bits | 1 bit
84 % of companies with a WAN are using MPLS
Notes: MPLS can be considered a Layer 2.5 networking protocol.
MPLS was created in the late 1990’s to avoid having routers waste time by having to stop and look up routing tables. The protocol allows most packets to be forwarded at the Layer 2 (switching) level rather than at the Layer 3(routing) level. Each packet gets labeled at the edge of the service provider's network and that label determines which pre-determined path the packet will follow. The paths, which are called label-switched paths (LSPs), allow service providers to decide ahead of time what will be the best way for certain types of traffic to flow within a private or public network. LSPs are virtual links
MPLS is protocol-independent.

## Slide 105: MPLS Components

## Slide 106: MPLS – Outside Traffic movement
Best parts of circuit switch and packet switch
Uses Labels to select predetermined “routes”
  Uses circuit-like techniques within ISP, and packet within Customer
Deploys VPN like features (customer packets remain “private”

## Slide 107: MPLS and the Internet

## Slide 108: Connecting to MPLS

## Slide 109: Multi-Service Ethernet
Ethernet connection into the WAN provider network
Use the big pipe for:
  MPLS, P2P or ethernet LAN, SIP (voice) trunks
Outbound only

## Slide 110: Due this week
1 post and 2 comments on d2l discussion
Submit to D2L your Web Assign 1
Research Memo 1 (be ready to discuss next week
Work on Web Assign 2 (not due for another week).